## Slide 1
AI PLANT OPERATIONS PLATFORM
Architecture Guide
Hyundai × PeopleTech
Edge-to-Cloud · 8 Use Cases · Integration-First
End-to-end platform architecture for AI-driven manufacturing
across Hyundai's global plant network
Plant Floor / Edge
Streaming & Integration
AI / ML Compute
Application & UX
Hyundai × PeopleTech · AI Manufacturing Practice · May 2026

## Slide 2
What is the AI Plant Operations Platform?
One platform, eight use cases, shared infrastructure
Edge-to-Cloud
Connects plant-floor sensors, cameras, and scanners through edge compute to cloud AI models. Sub-200ms line-side latency for real-time decisions. Runs on NVIDIA Jetson, Hailo, and Intel edge with AWS IoT Greengrass / Azure IoT Edge.
Integration-First
Plugs into Hyundai's existing SAP MES/ERP, SAP PM, AVEVA PI historian — no rip-and-replace. Pre-built connector library with standardized event schemas for line-hold, work-order generation, and quality events.
8 AI Use Cases
Visual Inspection — CNN defect detection
Variant Confirmation — VIN/BOM match
Seating Validation — fitment checks
SOP Compliance — pose estimation
Predictive Quality — sensor fusion ML
Predictive Maintenance — anomaly detection
Safety Monitoring — PPE/zone AI
Digital Traceability — genealogy graph
Designed to pilot on one line and scale across Ulsan, Asan, HMGMA, HMMA, HMMC, HMI.
Shared infrastructure · Shared MLOps · Scale from 1 line to enterprise

## Slide 3
The Problem
Why siloed solutions fail at plant scale
Siloed Point
Solutions
→
Fragmented
Data
→
Slow Response
Times
→
High Cost of
Quality Failures
No Shared Platform
Each use case built on its own stack. Separate cameras, separate databases, separate dashboards. No cross-use-case data fusion. Infrastructure cost multiplied by 8.
Integration Gap
AI models produce insights that never reach operators. Manual hand-offs between AI outputs and SAP/MES. No automated line-hold, work-order generation, or escalation.
Latency & Scale
Cloud-only inference adds 500ms–2s latency — too slow for line-side decisions. Models trained once, never retrained. No OTA update path. Scaling from 1 line to 50 requires re-architecture.
The platform approach: one infrastructure, eight use cases, one integration layer

## Slide 4
Architecture Overview
Four-layer edge-to-cloud platform
PLANT FLOOR / EDGE CAPTURE
Vision Cameras
(Cognex, Basler)
IoT Sensors
(Vib, Acoustic)
RFID / Barcode
Scanners
Edge Compute
(Jetson, Hailo)
STREAMING & INTEGRATION
Kafka Event
Stream
SAP MES / ERP
Connectors
AVEVA PI
Historian
Quality DB
Neo4j Graph
AI / ML COMPUTE (CLOUD)
SageMaker /
Azure ML
8 Use Case
Model Groups
MLOps
Pipeline
Data Lake /
Feature Store
APPLICATION & UX
Quality
Dashboard
Asset Health
Dashboard
EHS / Safety
Wall
Executive BI
& Alerts
5-Step Data Flow
1. Capture — cameras, sensors, RFID scan production line
2. Edge Inference — local GPU runs models in <200ms
3. Event Stream — Kafka routes scored events to integration layer
4. AI + Enterprise — cloud models train; SAP/MES act on events
5. UX — dashboards, alerts, and mobile push to operators

## Slide 5
Components Deep Dive
What each layer does and why
Plant Floor / Edge Capture
Vision cameras (Cognex, Basler, Keyence) — multi-angle, high-res surface capture
IoT sensors — vibration, acoustic, thermal, pressure for machine health
RFID & barcode scanners — component tracking and VIN verification
Edge compute (NVIDIA Jetson, Hailo) — <200ms local inference
OPC-UA bus + edge gateway — protocol translation and local resilience
Streaming & Integration
Kafka event bus — real-time quality, maintenance, safety event routing
MES / SAP Connector Library — pre-built line-hold and work-order integration
SAP MES/ERP + SAP PM/CMMS — production orders, maintenance scheduling
AVEVA PI historian — time-series sensor storage
Neo4j genealogy graph — component-to-vehicle traceability
AI / ML Compute (Cloud)
AWS SageMaker / Azure ML — training, tuning, model registry
8 model groups: CNN (visual), YOLO (detection), LSTM (time-series), Autoencoder (anomaly)
MLOps: MLflow + CI/CD + drift detection + auto-retraining
Model optimization: TensorRT / ONNX → edge OTA deployment
Data lake (S3 / ADLS) with Parquet / Delta Lake feature store
Application & UX
Quality dashboard — real-time defect monitoring by station/shift
Asset health dashboard — risk-prioritized maintenance work queue
EHS live wall — PPE compliance, zone alerts, incident reports
Operator station UI — pass/fail cues, hold-station controls
Alerting (Slack/Teams/Andon) + Executive BI (Power BI/Tableau)

## Slide 6
Platform vs. Point Solutions
Why a unified architecture wins
Dimension
Siloed Point Solutions
Unified Platform (Ours)
Infrastructure cost
8× separate stacks, cameras, DBs
Shared edge fleet + one data lake
Integration effort
Custom connectors per use case
Pre-built SAP/MES library, Kafka bus
Latency
Cloud-only: 500ms–2s
Edge-first: <200ms
Model retraining
Manual, ad-hoc per model
Unified MLOps: drift detect → auto-retrain → OTA
Time to add use case
3–6 months from scratch
4–6 weeks (deploy model to existing infra)
Cross-UC data fusion
Not possible
Shared data lake enables sensor + vision fusion
Scale path
Re-architect per plant
Add edge nodes, same stack

## Slide 7
Implementation View
Edge inference + MLOps pipeline
Edge Inference Pipeline
Camera captures frame → edge GPU runs TensorRT-optimized model
Anomaly score + metadata published to Kafka topic
If score > threshold → MES connector triggers SAP line-hold
Defect record persisted to PostgreSQL with full traceability
Dashboard updates in real time; operator sees pass/fail
MLOps Retraining Loop
Rework-confirmed defects feed back to SageMaker weekly
MLflow tracks experiments, model registry versions artifacts
TensorRT optimization → OTA push to edge fleet via Greengrass
# Edge Inference Pipeline (simplified)
# ─────────────────────────────────────
frame = camera.capture() # Cognex/Basler
tensor = preprocess(frame) # Resize, normalize
score = model.infer(tensor) # TensorRT on Jetson
event = {
"station_id": STATION,
"score": score,
"timestamp": now(),
"image_ref": s3_upload(frame),
"vin": rfid_reader.last_scan()
}
kafka.publish("quality.defects", event)
if score > THRESHOLD:
mes_connector.trigger_line_hold(
station=STATION,
reason="AI defect detected",
score=score
)
quality_db.insert(event)
alerting.notify(SUPERVISOR, event)
# ── Weekly retraining loop ──
rework_data = quality_db.get_confirmed()
sagemaker.train(
dataset=rework_data,
base_model="resnet50-v3.2",
output="s3://models/resnet50-v3.3"
)
iot_greengrass.ota_deploy("resnet50-v3.3")

## Slide 8
Expected Outcomes
Measured results from peer-OEM deployments
Platform Impact Areas
Visual Inspection
CNN defect detection → −45% rework, −60% escapes
Predictive Maintenance
Anomaly detection → −40% downtime, 5:1 ROI
Safety & SOP
Pose estimation → −55% incidents, 98% PPE compliance
Traceability
Genealogy graph → 100% tracking, recall in days
<200ms
Edge inference latency — line-side decisions in real time
3–5×
Measured ROI within first year of deployment
40–60%
Faster time-to-pilot with PeopleTech accelerators

## Slide 9
Key Data Flow
How a defect detection event moves through the platform
1
Camera
Capture
High-res frame
in light tunnel
→
2
Edge
Inference
CNN model
<200ms
→
3
Event
Publish
Kafka topic
with score
→
4
MES
Line-Hold
SAP API
auto-trigger
→
5
Quality DB
Write
PostgreSQL
traceability
→
6
Dashboard
Update
Real-time
operator UI
→
7
Retrain
& OTA
SageMaker
→ Edge push
Predictive Maintenance Flow
1
Sensor
Stream
Vibration, acoustic
thermal data
→
2
Edge
Aggregate
Windowed
features
→
3
Anomaly
Detect
Autoencoder
+ survival model
→
4
Work Order
Generate
SAP PM
auto-create
→
5
Technician
Notify
Mobile push
+ risk queue

## Slide 10
Summary & Next Steps
Unified Platform
One infrastructure for 8 use cases. Shared edge compute, event bus, data lake, and MLOps pipeline. Adding a new use case is a model deployment — not an infrastructure project. Amortize cost across the entire program.
Integration-First
Plugs into SAP MES/ERP, SAP PM, AVEVA PI — no rip-and-replace. AI outputs flow into the systems operators already use. Automated line-hold, work-order generation, and escalation. Pre-built connector library cuts integration time 40–60%.
Pilot-First Scale
Start with 2 pilots on one line: Visual Inspection at HMGMA (IONIQ paint) + Predictive Maintenance at Ulsan stamping. Prove ROI in 12 weeks. Scale to plant-wide without re-architecture. Go/no-go gate before any commitment to expand.
Key Design Decisions
Edge-first inference — <200ms latency for real-time line-side decisions
Cloud retraining — weekly model improvement with drift detection and auto-retrain
Shared data lake — enables cross-use-case fusion (e.g., vision + sensor for predictive quality)
Modular add-a-use-case — deploy model to existing infra in 4–6 weeks vs. 3–6 months from scratch
Next step: Pilot Scoping Workshop — walk the line, agree the baseline, lock dates.